## Slide 1: Dynamic Speech MRI at 0.55 T: Off-Resonance Physics and Gradient Trade-offs for Extended Spiral Readouts
Swati Ramtilak1, Ute Gorke2, Sean Fain1, Sajan Goud Lingala1
1University of Iowa, Iowa City, USA
2Siemens Healthineers, USA

## Slide 2: Upper Airway Complex

## Slide 3: Spatial vs Time Resolution: Speech MRI
Lingala, Sajan Goud, et al. "Recommendations for real‐time speech MRI." Journal of Magnetic Resonance Imaging 43.1 (2016): 28-44.

## Slide 4: Dynamic speech MRI
3 T
1.5 T
0.55 T

## Slide 5: Dynamic speech MRI
Sutton, Bradley P., et al. "Faster dynamic imaging of speech with field inhomogeneity corrected spiral fast low angle shot (FLASH) at 3 T."
Field map
Image
3 T
1.5 T
0.55 T

## Slide 6: Dynamic speech MRI
3 T
1.5 T
0.55 T
Radial readouts (<1.2 ms)
Burdumy, JMRI 2016
2D dMRI
Spiral navigators
Cartesian readouts (<1.2 ms)
Jin et al, MRM 2024
3D dMRI

## Slide 7: Dynamic speech MRI
3 T
1.5 T
0.55 T
Radial readouts (<1.2 ms)
Burdumy, JMRI 2016
2D dMRI
Spiral navigators
Cartesian readouts (<1.2 ms)
Jin et al, MRM 2024
3D dMRI
Spiral readouts (<2.4 ms)
Lingala et al, MRM 2016
Zhao et al, MRM 2021
3D dMRI
2D dMRI

## Slide 8: Dynamic speech MRI
3 T
1.5 T
0.55 T
Radial readouts (<1.2 ms)
Burdumy, JMRI 2016
2D dMRI
Spiral navigators
Cartesian readouts (<1.2 ms)
Jin et al, MRM 2024
3D dMRI
Spiral readouts (<2.4 ms)
Lingala et al, MRM 2016
Zhao et al, MRM 2021
3D dMRI
2D dMRI
8.9 ms spiral readouts
5.3 ms spiral readouts
bSSFP
GRE

## Slide 9: To assess whether dynamic speech MRI can be achieved at 0.55 T using commercial gradients (Siemens Free max)
Purpose

## Slide 10: Goal: To design multi shot spirals
20 cm
2.2 mm x 2.2mm
Tongue
Velum
lips
epiglottis
glottis
20 cm
16 arms for full sampling

## Slide 11: Implementation with varying gradient specifications
Slew rate= 150 T/m/s , Gmax = 80 mT/m, tread = 2.3 ms
Example gradient waveforms for 16 spiral arms
High performance Gradients

## Slide 12: Implementation with varying gradient specifications
Slew rate= 30 T/m/s , Gmax = 12 mT/m, tread = 5.3 ms
Example gradient waveforms for 16 spiral arms
Commercial Gradients
Slew rate= 150 T/m/s , Gmax = 80 mT/m, tread = 2.3 ms
High performance Gradients

## Slide 13: Implementation with varying gradient specifications
Slew rate= 30 T/m/s , Gmax = 12 mT/m, tread = 5.3 ms
Example gradient waveforms for 16 spiral arms
Commercial Gradients
Slew rate= 150 T/m/s , Gmax = 80 mT/m, tread = 2.3 ms
High performance Gradients

## Slide 14: Uniform-density spirals implemented at 0.55T and 3T
Number of spiral arms for full sampling | 27 | 16 | 11 | 9
3 Tesla (Slew rate = 150 T/m/s, Gmax = 80 mT/m ) |  |  |  | 
Readout duration (ms) | 1.48 | 2.344 | 3.308 | 3.992
TR (ms) | 6 | 6.5 | 7.5 | 8
Siemens FreeMax 0.55 T(Slew rate= 30 T/m/s , Gmax = 12 mT/m) |  |  |  | 
Readout duration (ms) | 3.588 | 5.32 | 7.38 | 8.89
TR (ms) | 7.1 | 9.1 | 12 | 14
FOV= 20 × 20 cm², resolution = 2.27 × 2.27 mm², slice thickness = 8 mm

## Slide 15: Uniform-density spirals implemented at 0.55T and 3T
Number of spiral arms for full sampling | 27 | 16 | 11 | 9
GE Premier 3T(Slew rate = 150 T/m/s, Gmax = 80 mT/m ) |  |  |  | 
Readout duration (ms) | 1.48 | 2.344 | 3.308 | 3.992
TR (ms) | 6 | 6.5 | 7.5 | 8
Siemens FreeMax 0.55 T(Slew rate= 30 T/m/s , Gmax = 12 mT/m) |  |  |  | 
Readout duration (ms) | 3.588 | 5.32 | 7.38 | 8.89
TR (ms) | 7.1 | 9.1 | 12 | 14
FOV= 20 × 20 cm², resolution = 2.27 × 2.27 mm², slice thickness = 8 mm

## Slide 16: Experiments
2 volunteers were imaged
0.55 T (commercial gradients) and 3 T (high performing gradients)
Speech tasks: za-na-za (interleaved consonant vowel sounds) and fluent rapid speech counting numbers
Custom 16 channel coil utilized on the 3T
Flex 6 channel coil utilized on the 0.55 T
Continuous golden angle interleaving (mid-sagittal imaging)
View-sharing and spatio-temporal total variation reconstruction was implemented at varying under-sampling factors

## Slide 17
Results

## Slide 18: View-sharing reconstructions - subject uttering the phrase /za/-/na/-/za/
18
27 arms | 16 arms | 11 arms | 9 arms
tread=3.58 ms
t foot print=191.7 ms
0.55T Free max
Slew rate= 30 T/m/s Gmax = 12 mT/m
FOV= 20 × 20 cm², resolution = 2.27 × 2.27 mm², slice thickness = 8 mm

## Slide 19: View-sharing reconstructions - subject uttering the phrase /za/-/na/-/za/
19
27 arms | 16 arms | 11 arms | 9 arms
tread=3.58 ms
t foot print=191.7 ms
tread=5.32 ms
t foot print=145.6 ms
tread=7.38 ms
t foot print=132 ms
tread=8.89 ms
t foot print=126 ms
0.55T Free max
Slew rate= 30 T/m/s Gmax = 12 mT/m
Robust to off-resonance blur at 0.55 T even at tread = 8.89 ms
FOV= 20 × 20 cm², resolution = 2.27 × 2.27 mm², slice thickness = 8 mm

## Slide 20
3T
Slew rate = 150 T/m/s Gmax = 80 mT/m
27 arms | 16 arms | 11 arms | 9 arms
Number of spiral arms for full sampling
tread=1.48 ms
t foot print=162 ms
tread=3.58 ms
t foot print=191.7 ms
tread=5.32 ms
t foot print=145.6 ms
tread=7.38 ms
t foot print=132 ms
tread=8.89 ms
t foot print=126 ms
0.55T Free max
Slew rate= 30 T/m/s Gmax = 12 mT/m
Robust to off-resonance blur at 0.55 T even at tread = 8.89 ms
20

## Slide 21
tread=2.48 ms
t foot print=104 ms
velum
blurred
3T
Slew rate = 150 T/m/s Gmax = 80 mT/m
27 arms | 16 arms | 11 arms | 9 arms
Number of spiral arms for full sampling
tread=1.48 ms
t foot print=162 ms
tread=3.99 ms
t foot print=72 ms
signal loss
tongue
dorsum
blurred
tread=3.30 ms
t foot print=82.5 ms
velum
blurred
Pronounced off-resonance induced artifacts at 3T for tread >1.48 ms
tread=3.58 ms
t foot print=191.7 ms
tread=5.32 ms
t foot print=145.6 ms
tread=7.38 ms
t foot print=132 ms
tread=8.89 ms
t foot print=126 ms
0.55T Free max
Slew rate= 30 T/m/s Gmax = 12 mT/m
Robust to off-resonance blur at 0.55 T even at tread = 8.89 ms
21

## Slide 22: Comparing View Sharing and Constrained Reconstruction
22
View sharing
Spatio temporal total variation reconstruction(rate 4)
t foot print=145.6 ms
t foot print=36.4 ms
16 arms
tongue tip
Subtle motion blur with tongue tip and velum movements
Speech Task /za/na/za/
lower lip
velum

## Slide 23: Constrained Reconstruction
23
Constrained reconstruction
(rate 8)
Constrained reconstruction
(rate 6)
Constrained reconstruction
(rate 4)
Dynamic images
Image time profile
sharper time profile
rapid transitions blurred
faint alias artifacts
t foot print=36.4 ms
t foot print=27.3 ms
t foot print=18.2 ms
Speech Task rapid number counting

## Slide 24: Conclusion
24
This work
Free-Max 0.55 T
Off-resonance tolerance at low field permits extended spiral readouts with negligible signal loss upto a readout duration of ~9ms
Spatio-temporal TV constraint-based reconstruction provided temporal footprints up to 18–36ms.

## Slide 25: Acknowledgments
NIH NHLBI: R01 HL173483
NIH-S10 instrumentation grant: 1S10OD025025-01